Anatomy of a mikroPascal for PIC32 application

## Introduction
Take this simple program,

program MyProject;

{ Declarations section }

begin
  { Main program }
  LATA0_bit := not LATA0_bit
end.

In this example the EBASE value is equal to 0x9FC01000

What does the compiler actually do?

If you look at the listing you see the following functions:

0x9D000000 [32] ___CC2DW
0x9D000020 [24] ___GenExcept
0x9D000038 [24] ___BootGenExcept
0x9D000050 [44] _main
0xBFC00000 [296] ___BootStartUp

So what does all this mean? In a PIC32 there are virtual memory spaces:

Start Address	Size (bytes)	Partition	Kind	Comments
0x7D000000 + BMXPUPBA	BMXPFMSZ - BMXPUPBA	USEG/KUSEG	Program Flash
0x7F000000	BMXPFMSZ - BMXPUPBA	USEG/KUSEG	Data RAM
0x7F000000	BMXPFMSZ - BMXPUPBA	USEG/KUSEG	Program RAM
0x80000000	BMXDKPBA (max 128 K)	KSEG0 (cacheable)	Program Flash	same physical address as KSEG1 data RAM
0x80000000 + BMXDKPBA	BMXDUDBA - BMXDKPBA	KSEG0 (cacheable)	Data RAM	same physical address as KSEG1 program RAM
0x9D000000	BMXPUPBA (max 512 K)	KSEG0 (cacheable)	Program RAM	same physical address as KSEG1 program flash
0xA0000000	BMXPUPBA (max 128 K)	KSEG1	Program Flash
0xA0000000 + BMXDKPBA	BMXDUDBA - BMXDKPBA	KSEG1	Data RAM
0xBD000000	BMXPUPBA (max 512 K)	KSEG1	Program RAM
0xBF800000	1 MB	kernel (KSEG1, non-cacheable)	Peripheral SFRs
0xBFC00000	12 KB	kernel (KSEG1, non-cacheable)	Boot flash

In a mikroElectronika (mE) application the BMX___ values are left at default 0.

## Exceptions and Interrupts

If you look at the listing for the program you also find 2 more magic functions:

____SysVT:
0x9FC01180 0x0B400008 J ___GenExcept
0x9FC01184 0x70000000 NOP
; end of ____SysVT

____BootVT:
0xBFC00380 0x3C1E9D00 LUI R30, 40192
0xBFC00384 0x37DE0038 ORI R30, R30, 56
0xBFC00388 0x03C00008 JR R30
0xBFC0038C 0x70000000 NOP
; end of ____BootVT

Lets look at the ___SysVT call first

____SysVT:
0x9FC01180 0x0B400008 J ___GenExcept

where

0x9D000020 [24] ___GenExcept

What is special about this memory space (0x9FC01180)? Notice it is our EBASE+0x180... So what? If you look at the MIPS documentation you will find the answers (these documents can be found in the Open mikroBootloader SourceForge repository under Documentation). This is the address where if a general exception occurs the processor will jump to. The mE compiler simple jumps to the ___GenExecpt function without putting a return address on the stack. The default exception handlers is as follows:

___GenExcept:
;__Lib_System.mpas, 90 ::
0x9D000020	0x27BDFFFC ADDIU	SP, SP, -4
;__Lib_System.mpas, 91 ::
L____GenExcept20:
0x9D000024	0x0B400009 J	L____GenExcept20
0x9D000028	0x70000000 NOP
;__Lib_System.mpas, 93 ::
L_end___GenExcept:
0x9D00002C	0x27BD0004 ADDIU	SP, SP, 4
0x9D000030	0x42000018 ERET
0x9D000034	0x70000000 NOP
; end of ___GenExcept

The handler manually removes 4 bytes from the stack and loops forever. Also note that a simple jump to the function can be made because both of these addresses are in the KSEG0 space.

What else is interesting about this address? If you look at the table this is beyond the KSEG0 0x9D000000 + MAX_512k_Bytes. This address is mapping into the Boot Flash area through the KSEG0. This means that the exception and interrupt tables will be place in Boot Flash through the KSEG0 address space. It is not clear to me why this is done.

Now lets look at the ___BootVT call

____BootVT:
0xBFC00380 0x3C1E9D00 LUI R30, 40192
0xBFC00384 0x37DE0038 ORI R30, R30, 56
0xBFC00388 0x03C00008 JR R30
0xBFC0038C 0x70000000 NOP
; end of ____BootVT

First off notice this is located in the Boot Flash (see the virtual memory table) but at an offset. What is special about this offset? Again the MIPS documentation comes to the rescue. This becomes complicated based on the setting of the Status and Cause registers. Depending on configuration this can be the exception jump target of TLB Refill, Interrupt, and All Others.

A typical mE program is configures its CP0 Status and Cause register as follow:

Register and Bit	Control	MikroElectronika Default
CP0_STATUS / Bit 22	BEV: Bootstrap Exception Vector Control bit / Controls the location of exception vectors. / 1 = Bootstrap / 0 = Normal	0 = Normal
CP0_STATUS / bit 1	EXL: Exception Level bit / Set by the processor when any exception other than Reset, Soft Reset, or NMI exceptions is taken. / 1 = Exception level / 0 = Normal level / When EXL is set: / • Processor is running inKernel mode / • Interrupts are disabled	1 = Exception level / when an exception is encountered
CP0_CAUSE / bit 23	IV: Interrupt Vector bit / Indicates whether an interrupt exception uses the general exception vector or a special interrupt vector / 1 = Use the special interrupt vector (0x200) / 0 = Use the general exception vector (0x180) / If the IV bit (Cause<23>) is ‘1’ and the BEV bit (Status<22>) is ‘0’, the special interrupt vector represents the base of the vectored interrupt table.	1 = Use the special interrupt vector (0x200)

To summarize a mE application will setup the exceptions and interrupts as follows:

Exception	Vector
Reset, Soft, Reset, NMI	0xBFC00000	Boot Flash
TBL Refill	EBASE+0x180	KSEG0 (cacheable) [EXL = 1 when exception occurs]
Cache Error	EBASE+0x180??	KKSEG0 (cacheable) [EXL = 1 when exception occurs]
Interrupts	EBASE+0x200+Interrupt Vector	ME default 0x9FC01000 (KSEG0)

So what it appears is that ___BootVT is a defensive function that is not used unless the CP0_StatusBEV
bit has been changed by the application. Lastly note that the jump is more complicated:

____BootVT:
0xBFC00380 0x3C1E9D00 LUI R30, 40192
0xBFC00384 0x37DE0038 ORI R30, R30, 56
0xBFC00388 0x03C00008 JR R30
0xBFC0038C 0x70000000 NOP
; end of ____BootVT

It loads 0x9D000038 into R30 then jumps. This is necessary because the current execution is within the Boot Flash and the Jump is into the KSEG0 flash. This is the address of

0x9D000038 [24] ___BootGenExcept

___BootGenExcept:
;__Lib_System.mpas, 84 ::
0x9D000038	0x27BDFFFC ADDIU	SP, SP, -4
;__Lib_System.mpas, 85 ::
L____BootGenExcept14:
0x9D00003C	0x0B40000F J	L____BootGenExcept14
0x9D000040	0x70000000 NOP
;__Lib_System.mpas, 87 ::
L_end___BootGenExcept:
0x9D000044	0x27BD0004 ADDIU	SP, SP, 4
0x9D000048	0x42000018 ERET
0x9D00004C	0x70000000 NOP
; end of ___BootGenExcept

This also loops for ever when the exception is entered.

Now lets throw in an interrupt and see if it does what we expect with Vector Spacing of 32...

program MyProject;

{ Declarations section }

procedure CoreTimer(); iv IVT_CORE_TIMER; ilevel 7; ics ICS_AUTO;
begin
end;

procedure Timer1(); iv IVT_TIMER_1; ilevel 7; ics ICS_AUTO;
begin
end;

procedure InputCapture1(); iv IVT_INPUT_CAPTURE_1; ilevel 7; ics ICS_AUTO;
begin
end;

begin
  { Main program }
  LATA0_bit := not LATA0_bit
end.

;Address Opcode	ASM
____SysVT:
0x9FC01180	0x0B40004F J	___GenExcept
0x9FC01184	0x70000000 NOP
0x9FC01188	0x70000000 NOP
0x9FC0118C	0x70000000 NOP
0x9FC01190	0x70000000 NOP
0x9FC01194	0x70000000 NOP
0x9FC01198	0x70000000 NOP
0x9FC0119C	0x70000000 NOP
0x9FC011A0	0x70000000 NOP
0x9FC011A4	0x70000000 NOP
0x9FC011A8	0x70000000 NOP
0x9FC011AC	0x70000000 NOP
0x9FC011B0	0x70000000 NOP
0x9FC011B4	0x70000000 NOP
0x9FC011B8	0x70000000 NOP
0x9FC011BC	0x70000000 NOP
0x9FC011C0	0x70000000 NOP
0x9FC011C4	0x70000000 NOP
0x9FC011C8	0x70000000 NOP
0x9FC011CC	0x70000000 NOP
0x9FC011D0	0x70000000 NOP
0x9FC011D4	0x70000000 NOP
0x9FC011D8	0x70000000 NOP
0x9FC011DC	0x70000000 NOP
0x9FC011E0	0x70000000 NOP
0x9FC011E4	0x70000000 NOP
0x9FC011E8	0x70000000 NOP
0x9FC011EC	0x70000000 NOP
0x9FC011F0	0x70000000 NOP
0x9FC011F4	0x70000000 NOP
0x9FC011F8	0x70000000 NOP
0x9FC011FC	0x70000000 NOP
0x9FC01200	0x0B40002C J	_CoreTimer
0x9FC01204	0x70000000 NOP
0x9FC01208	0x70000000 NOP
0x9FC0120C	0x70000000 NOP
0x9FC01210	0x70000000 NOP
0x9FC01214	0x70000000 NOP
0x9FC01218	0x70000000 NOP
0x9FC0121C	0x70000000 NOP
0x9FC01220	0x0B40003E J	_main
0x9FC01224	0x70000000 NOP
0x9FC01228	0x70000000 NOP
0x9FC0122C	0x70000000 NOP
0x9FC01230	0x70000000 NOP
0x9FC01234	0x70000000 NOP
0x9FC01238	0x70000000 NOP
0x9FC0123C	0x70000000 NOP
0x9FC01240	0x0B40003E J	_main
0x9FC01244	0x70000000 NOP
0x9FC01248	0x70000000 NOP
0x9FC0124C	0x70000000 NOP
0x9FC01250	0x70000000 NOP
0x9FC01254	0x70000000 NOP
0x9FC01258	0x70000000 NOP
0x9FC0125C	0x70000000 NOP
0x9FC01260	0x0B40003E J	_main
0x9FC01264	0x70000000 NOP
0x9FC01268	0x70000000 NOP
0x9FC0126C	0x70000000 NOP
0x9FC01270	0x70000000 NOP
0x9FC01274	0x70000000 NOP
0x9FC01278	0x70000000 NOP
0x9FC0127C	0x70000000 NOP
0x9FC01280	0x0B40001A J	_Timer1
0x9FC01284	0x70000000 NOP
0x9FC01288	0x70000000 NOP
0x9FC0128C	0x70000000 NOP
0x9FC01290	0x70000000 NOP
0x9FC01294	0x70000000 NOP
0x9FC01298	0x70000000 NOP
0x9FC0129C	0x70000000 NOP
0x9FC012A0	0x0B400008 J	_InputCapture1
0x9FC012A4	0x70000000 NOP
0x9FC012A8	0x70000000 NOP
0x9FC012AC	0x70000000 NOP
0x9FC012B0	0x70000000 NOP
0x9FC012B4	0x70000000 NOP
0x9FC012B8	0x70000000 NOP
0x9FC012BC	0x70000000 NOP
0x9FC012C0	0x0B40003E J	_main
0x9FC012C4	0x70000000 NOP
0x9FC012C8	0x70000000 NOP
0x9FC012CC	0x70000000 NOP
0x9FC012D0	0x70000000 NOP
0x9FC012D4	0x70000000 NOP
0x9FC012D8	0x70000000 NOP
0x9FC012DC	0x70000000 NOP
0x9FC012E0	0x0B40003E J	_main
0x9FC012E4	0x70000000 NOP
0x9FC012E8	0x70000000 NOP
0x9FC012EC	0x70000000 NOP
…..
0x9FC0183C	0x70000000 NOP
0x9FC01840	0x0B40003E J	_main
0x9FC01844	0x70000000 NOP
0x9FC01848	0x70000000 NOP
0x9FC0184C	0x70000000 NOP
0x9FC01850	0x70000000 NOP
0x9FC01854	0x70000000 NOP
0x9FC01858	0x70000000 NOP
0x9FC0185C	0x70000000 NOP
0x9FC01860	0x0B40003E J	_main
0x9FC01864	0x70000000 NOP
; end of ____SysVT

The ___SysVT has grown to handle all the interrupt vectors. It is interesting that if you enable an interrupt in code but not have a handler for it your application will restart with the first line in the main program block of code.

Selecting Single Interrupt Handler in the options does exactly that:

program MyProject;

{ Declarations section }

procedure SingleHandler(); iv IVT_CORE_TIMER; ilevel 7; ics ICS_AUTO;
begin
end;

begin
  { Main program }
  LATA0_bit := not LATA0_bit
end.

;Address Opcode	ASM
____SysVT:
0x9FC01180	0x0B400008 J	___GenExcept
0x9FC01184	0x70000000 NOP
0x9FC01188	0x70000000 NOP
0x9FC0118C	0x70000000 NOP
0x9FC01190	0x70000000 NOP
0x9FC01194	0x70000000 NOP
0x9FC01198	0x70000000 NOP
0x9FC0119C	0x70000000 NOP
0x9FC011A0	0x70000000 NOP
0x9FC011A4	0x70000000 NOP
0x9FC011A8	0x70000000 NOP
0x9FC011AC	0x70000000 NOP
0x9FC011B0	0x70000000 NOP
0x9FC011B4	0x70000000 NOP
0x9FC011B8	0x70000000 NOP
0x9FC011BC	0x70000000 NOP
0x9FC011C0	0x70000000 NOP
0x9FC011C4	0x70000000 NOP
0x9FC011C8	0x70000000 NOP
0x9FC011CC	0x70000000 NOP
0x9FC011D0	0x70000000 NOP
0x9FC011D4	0x70000000 NOP
0x9FC011D8	0x70000000 NOP
0x9FC011DC	0x70000000 NOP
0x9FC011E0	0x70000000 NOP
0x9FC011E4	0x70000000 NOP
0x9FC011E8	0x70000000 NOP
0x9FC011EC	0x70000000 NOP
0x9FC011F0	0x70000000 NOP
0x9FC011F4	0x70000000 NOP
0x9FC011F8	0x70000000 NOP
0x9FC011FC	0x70000000 NOP
0x9FC01200	0x0B40000E J	_SingleHandler
0x9FC01204	0x70000000 NOP
; end of ____SysVT

In all cases the ___BootVT did not change

____BootVT:
0xBFC00380 0x3C1E9D00 LUI R30, 40192
0xBFC00384 0x37DE0038 ORI R30, R30, 56
0xBFC00388 0x03C00008 JR R30
0xBFC0038C 0x70000000 NOP
; end of ____BootVT
## Program Flow
The MIPS processor start execution in the Flash Memory space at 0xBFC00000, lets look at our functions in the listing:
0x9D000000 [32] ___CC2DW
0x9D000020 [24] ___GenExcept
0x9D000038 [24] ___BootGenExcept
0x9D000050 [44] _main
0xBFC00000 [296] ___BootStartUp

Yup there it is ___BootStartup. This function does a lot of interesting things that get the processor in the state the compiler expects it to be in.

___BootStartUp:
;__Lib_System.mpas, 96 ::
0xBFC00000	0x27BDFFFC ADDIU	SP, SP, -4
;__Lib_System.mpas, 100 ::
0xBFC00004	0x70000000 NOP
….
….
0xBFC0010C	0x409E6800 MTC0	R30, 13, 0
;__Lib_System.mpas, 178 ::
0xBFC00110	0x3C1E9D00 LUI	R30, #hi_addr(_main+0)
;__Lib_System.mpas, 179 ::
0xBFC00114	0x37DE0050 ORI	R30, R30, #lo_addr(_main+0)
;__Lib_System.mpas, 181 ::
0xBFC00118	0x03C00008 JR	R30
;__Lib_System.mpas, 182 ::
0xBFC0011C	0x70000000 NOP
;__Lib_System.mpas, 184 ::
L_end___BootStartUp:
0xBFC00120	0x03E00008 JR	RA
0xBFC00124	0x27BD0004 ADDIU	SP, SP, 4
; end of ___BootStartUp

The most interesting thing for us the the last few lines where the address of the _main function is loaded and jumped to with a return address stored.

The _CC2DW function is a general purpose function that the compiler links in to set various settings as needed and initialize variable that the compiler knows about is some special way. The reason it was linked into this listing was because all libraries were checked so it was being called out of something in the library system to initialize them. Once all libraries were unchecked this function was eliminated from the listing.

Lets recap:

- A stub is placed at the 2 possible places an exception or interrupt can be called in a MIPS processor
- One is in the KSEG0 addressed Flash (but it is at a high enough address that is exists in the Boot Flash) and one is in the Boot Flash as a MIPS processor documentation explains
- Exceptions and Interrupts are handled in the KSEG0 addressed Flash
- The Boot Flash Exception stub seems to be only to protect against the CP0_Status and CP0_Cause bits being manipulated by the application and forcing the exceptions to be handled in the Boot Flash
- Both Stubs point to functions that are addressed in the KSEG0 space